## Slide 1: AWS Network
Add Partner logo

## Slide 2: Amazon VPC

## Slide 3
Subnet A2
Subnet B2
Instance
Instance
US-EAST-1
VPC
Availability Zone A
Availability Zone B
Subnet A1
Subnet B1
10.0.0.0/24
10.0.1.0/24
10.0.2.0/24
10.0.3.0/24
10.0.0.0/16
Instance
Instance
REGION
AVAILABILITY ZONE
DATA CENTER, RACK, HOST
Amazon Virtual Private Cloud (VPC) overview

## Slide 4
Subnets
VPCs span a region
Subnets are allocated as a subset of the VPC CIDR range and span a specific AZ
You can have up to 200 subnets per VPC.
Implicit route between all subnets within a VPC
Subnet A2
Subnet B2
Instance
Instance
US-EAST-1
VPC
Availability Zone A
Availability Zone B
Subnet A1
Subnet B1
10.0.0.0/24
10.0.1.0/24
10.0.2.0/24
10.0.3.0/24
10.0.0.0/16
Instance
Instance

## Slide 5
Routing tables
Each subnet has associated routing table
Routing tables can be associated with multiple subnets
You can have 50 routes per route table.
Subnet A2
Subnet B2
Instance
Instance
US-EAST-1
VPC
Availability Zone A
Availability Zone B
Subnet A1
Subnet B1
10.0.0.0/24
10.0.1.0/24
10.0.2.0/24
10.0.3.0/24
10.0.0.0/16
Instance
Instance
RTB1
RTB1
RTB2
RTB2

## Slide 6
VPC to internet: Internet Gateway
Horizontally scaled, redundant, highly available VPC component
Connect your VPC Subnets to the Internet
Must be referenced on the Route Table
Performs 1:1 NAT between Public and Private IP Addresses
VPC
Public subnet
Route table
Internet gateway
Private subnet
Route table
Internet
EC2
Instance
Private IP: 10.0.0.1
Public IP: 198.51.100.2
EC2
Instance
Private IP: 10.1.1.1

## Slide 7
Public IP addressing: Elastic IP Address
Static, Public IPv4 address, associated with your AWS account
Dynamically assigned
Specific to a region
Can be associated with an instance or network interface
Can be remapped to another instance in your account
Useful for redundancy when Load Balancers are not an option
VPC
Public subnet
Internet gateway
Internet
EC2
Instance
Private IP: 10.0.0.1
Elastic IP: 198.51.100.2
EC2
Instance
Private IP: 10.0.0.2
Elastic IP: 198.51.100.2

## Slide 8
Outbound only traffic: NAT Gateway
Enable outbound connection to the internet
No incoming connection - useful for OS/packages updates, public web services access
Fully managed by AWS
Highly available
Up to 45Gbps aggregate bandwidth
Supports TCP, UDP, and ICMP protocols
Network ACLs apply to NAT gateway traffic
Public subnet
NAT gateway
VPC
Internet gateway
Private subnet
Internet
EC2
Instance
EC2
Instance
Private IP: 10.1.1.1
Route table

## Slide 9: VPC Security

## Slide 10
IP FW: Network Access Control List
Inbound and Outbound
Subnet level inspection
Optional level of security
By default, allow all traffic
Stateless
IP and TCP/UDP port based
Supports allow and deny rules
Deny all at the end
Private subnet
Public subnet
MySQL DB
Amazon Aurora
Amazon EC2
Network access control list
NACL “External Access”
Network access control list
NACL “Database Access”
0.0.0.0/0
HTTPS
(TCP 443)
10.0.0.0/16
MySQL
(TCP 3306)
Other IPs
Other Ports

## Slide 11
Resource FW: Security Groups
Stateful firewall
Inbound and Outbound customer defined rules
Instance/Interface level inspection
  Micro segmentation
  Mandatory, all instances have an associated Security Group
Can be cross referenced
  Works across VPC Peering
Only supports allow rules
  Implicit deny all if not allowed
Elastic Load Balancing (ELB)
Security group “Web ELB”
Security group “DB Tier”
MySQL DB
Amazon Aurora
VPC
“Web Tier”
MySQL
(TCP 3306)
Security group “Web Tier”
“Web ELB”
HTTP
(TCP 80)
HTTPS
(TCP 443)
Internet gateway
Amazon EC2
Web Server
Web Server

## Slide 12: Load Balancing

## Slide 13
Horizontal scaling: Elastic Load Balancing
Distribute traffic to multiple targets
  EC2 instances
  Containers
  IP addresses
  Lambda
Multiple Availability Zones
ELB Scales automatically
Support Auto Scaling Groups
  Automatically (de)register instances to the ELB based on health checks.
VPC
Internet gateway
EC2
Instance
EC2
Instance
EC2
Instance
ELB (public facing)
ELB (private facing)
Auto Scaling Group
EC2
Instance
EC2
Instance
EC2
Instance
EC2
Instance
Auto Scaling Group
EC2
Instance
Availability Zone A
Availability Zone B

## Slide 14
Types of ELB: NLB / ALB
Network Load Balancer (NLB)
Layer 4 Load Balancing
Connection-based Load Balancing
High Throughput
Low Latency
Preserve source IP address
Static IPs
Long-lived TCP Connections
Application Load Balancer (ALB)
Layer 7 Load Balancing
Content-Based Routing (host and path based)
HTTP/2 Support
Request Tracing
Web Application Firewall (WAF) integration
Application Load Balancer now supports TLS 1.3
Supported by both
Cross-zone load balancing
WebSocket Support
Deletion Protection

## Slide 15: VPC Connectivity Options

## Slide 16
Public subnet
Stay on AWS network: VPC Endpoints
Connect your VPC to:
  Supported AWS services
  VPC endpoint services powered by PrivateLink
Doesn’t require public IPs or Internet connectivity
Horizontally scaled, redundant, and highly available
Robust access control
Metrics for traffic visibility
VPC Endpoint
VPC
Internet gateway
Private subnet
EC2
Instance
EC2
Instance
VPC Endpoint
VPC
Service
Amazon
VPC PrivateLink
Network Load Balancer
(NLB)
VPC Endpoint
Amazon
Simple Storage Service (S3)
AWS
Key Management Service

## Slide 17
Connect multiple VPCs: VPC Peering
Scalable and high available
Supported between AWS accounts
Supported across AWS Regions
Bi-directional traffic
Remote Security groups can be referenced
Routing policy with Route Tables
  Not all subnets need to connect to each other
No overlapping IP addresses
No transitive routing
VPC
Public subnet
Private subnet
EC2
Instance
EC2
Instance
Route table
VPC Peering
VPC
Public subnet
Private subnet
EC2
Instance
EC2
Instance
Route table
Route table
Route table

## Slide 18
Connect multiple VPCs: Transit Gateway
Connect thousands of VPC across accounts within a region
Connect your VPCs and on-premises through a single transit gateway
Centralize VPN and AWS Direct Connect connections
Control segmentation and data flow with Route Tables
Hub and Spoke design
Up to 50 Gbps per attachment (burst)
AWS Transit Gateway
VPC
VPC
VPC
…
Routing Table A
Route table
Routing Table B
Route table
AWS Cloud
Shared Services VPC
VPC

## Slide 19: Connecting to On-premises

## Slide 20
VPN to AWS: Virtual Private Gateway
Fully managed VPN endpoint device
One Virtual Private Gateway per VPC
Redundant IPSec VPN Tunnels Terminating in different AZs
IPSec AES 256-bit encryption SHA-2 hashing
Scalable
Dynamic (BGP) or Static Routing
Default 10 Site-to-Site VPN connections per VGW – can increase limit
VPC
Corporate
data center
VGW (Virtual Private Gateway)
Customer gateway
VPN Connection
Availability Zone 1
Availability Zone 2
Internet
AWS Cloud

## Slide 21
Dedicated link to AWS: AWS Direct Connect
Dedicated network connection from your premises to AWS
Dedicated Connection (1,10 or 100 Gbps, Supports multiple VIFs)
AWS Partner Hosted Connection (50 Mbps to 10 Gbps, Single VIF)
Consistent Network Performance
  Dedicated bandwidth
  Low latency
Reduced egress data charges
Connect to 108 Direct Connection Locations across the globe
Corporate
data center
Customer gateway
AWS Direct Connect
Direct Connect
Location
AWS DX Device
AWS Cloud

## Slide 22
Dedicated link to AWS: AWS Direct Connect
For redundancy, DX can deployed with single or multiples:
  Circuits
  Providers
  Customer Gateways
  Direct Connect Locations
  Customer data centers
BGP Routing for redundancy
  AS Path Prepend
  Scope BGP Communities
  Local Preference BGP Communities
Corporate
data center
Customer gateway
AWS Direct Connect
Direct Connect
Location
AWS DX Device
AWS Cloud
AWS DX Device
Direct Connect
Location
AWS DX Device
AWS DX Device
Corporate
data center
Customer gateway

## Slide 23
Connect at global scale: DX Gateway + Transit Gateway
Transit VIF
  Connects to a AWS Transit Gateway
Simplify your network architecture and management overhead
Create a hub-and-spoke model that spans multiple
  VPCs
  Regions
  AWS accounts
VPC 1A
Corporate
data center
Customer gateway
AWS DX Device
AWS Cloud
VPC 1B
Region 1
VPC 2A
Region 2
Direct Connect
Location
AWS Transit Gateway
AWS Direct Connect
Gateway

## Slide 24: Domain Name Resolution

## Slide 25
How to solve my Domain Names to IP Address? Amazon Route 53
AWS DNS service
Domain Registration
Domain name resolution
100% availability SLA
Global routing:
  Health Checks
  DNS Failover
  Methods: Latency, Geography, IP/CIDR, Weighted Round Robin and Multivalue answer
Zone Apex integration
Public and private DNS
Amazon Route 53
Region us-east-1
(N. Virginia)
Region us-west-2
(Oregon)
Web Service
Elastic Load Balancer
Web Service
Elastic Load Balancer
Web Service
Elastic Load Balancer
Main Site Healthy
DNS Resolution Request
A/B Testing
App Version A
95% Traffic
App Version B
5% Traffic
App DR
Yes
No
Notes: Zone Apex integration
  ELB, S3, CloudFront
Note: Route 53 SLA is for the data plane; DR best practices: https://aws.amazon.com/blogs/networking-and-content-delivery/creating-disaster-recovery-mechanisms-using-amazon-route-53/

## Slide 26
Anycast instead of DNS: AWS Global Accelerator
Uses AWS Global Network from Edge to Region
Client traffic ingresses via closest available Edge location
Route client to closest healthy endpoint
No DNS switchover required, same IP address globally (Static IP Anycast)
AWS Cloud
Users in US
Users in Europe
Region us-east-1 (N. Virginia)
Region eu-west-1 (Ireland)
Edge location
Service
Elastic Load Balancer
Service
Elastic Load Balancer
Edge location
Edge location
Edge location
AWS Global Accelerator
www.example.com
IP: 198.51.100.2
www.example.com
IP: 198.51.100.2
Redundant path
Notes: Note: AWS Global Accelerator gives you two static anycast IP per accelerator

## Slide 27: For more information contact our team: xxx xxx xxx
Add Partner logo